## Slide 1
OB Cass Process Capacity Estimate: Public Large-Brewery Normalization
IMEN376 Proposal Support
Key idea: OB process data are private; normalize public large-lager benchmarks to an OB production proxy
1) OB production proxy
2024 Korea beer shipments 1,637,210 kL/year × OB home-market share 55.3% ≈ 905,377 kL/year = 9.05 million hL/year
2) Scale factor
OB proxy / Alrode capacity = 9.05 / 8.8 ≈ 1.029
3) Planning load
176,000 hL/week × 1.029 / 7 × 87% ≈ 22,505 hL/day = 7.5 standard batches/day
SAB Alrode Brewery
8.8 million hL/year 176,000 hL/week brewing 205,000 hL/week packaging 96 fermentation + 60 maturation vessels each vessel 3,000 hL
AB InBev Leuven / GEA
New cold block: 36 tanks 116 total tanks after expansion Tank sizes: 2,700–4,700 hL Centrifuge: 600–700 hL/hour
Steinecker / Krones
Steinecker mash filter: 14 brews/day output Krones bottle filler: up to 78,000 containers/hour
Normalization logic
Do not copy the plant-level 87% operating rate into every process. Use 87% only for planning load; estimate process capacities from equipment rated speeds or tank residence times.
Sources: SASSDA Alrode Brewery; GEA AB InBev Leuven; Steinecker mash filter; Krones filling lines

## Slide 2
Process Utilization: Bottleneck is the Fermentation-Centered Cold Block
2-page summary
Planning load = 7.5 standard batches/day. Capacity is estimated from process-specific public benchmarks.
Stage
Capacity
Util.
Interpretation
Milling/Mashing/Lautering
14.0 b/d
54%
Slack
Boiling/Cooling
12.0 b/d
63%
Not constraining
Fermentation
~8.0 b/d
94%
Primary bottleneck
Maturation
~8.6 b/d
87%
Secondary constraint
Final filtration
9.6–11.2 b/d
67–78%
Some slack
Bright beer holding
~13.0 b/d
58%
Buffer
Packaging
~10.0 b/d
75%
Slack
Utilization comparison
Milling/Mashing
Boiling/Cooling
Final filtration
Packaging
Maturation
Fermentation
85%
54%
63%
75%
75%
87%
94%
Conclusion: upstream brewing and packaging have line-speed slack, but fermentation ties up tanks for 13–14 days and reaches ~94% utilization. The dominant bottleneck is the fermentation-centered cold block.